## Slide 1: NATURAL GAS Niels Mejía Ibarra
UNIVERSIDAD NACIONAL DE INGENIERÍA
FACULTAD DE PETRÓLEO, GAS NATURAL Y PETROQUÍMICA

## Slide 2: COGENERATION UNIT
A cogeneration unit, also known as a combined heat and power (CHP) system, is an energy-efficient system that simultaneously generates electricity and useful thermal energy from a single fuel source. This dual-generation process makes cogeneration units highly efficient compared to traditional methods of electricity and heat production, which are typically separate and less efficient.

## Slide 3
BOILER
TURBINE
PROCESSING UNITS AND EQUIPMENT (1)
NATURAL GAS = 21.5 BFOE
FUEL GAS = 504.3 BFOE
FLEXIGAS = 3,133.8 BFOE
LIGHT NAPHTHA = 0 BBL
PROCESS WATER
VERY HIGH PRESSURE STEAM
PHOSPHATE
PROCESSING UNITS AND EQUIPMENT (2)
ELECTRIC POWER
HIGH PRESSURE STEAM
MEDIUM PRESSURE STEAM
DRAINAGE
CONDENSATE + LOW PRESSURE STEAM
ATMOSPHERE
EXHAUST GASES (*)
Carbon Dioxide (CO2)
Water Vapor (H2O)
Carbon Monoxide (CO)
Nitrogen Oxides (NOx)
Unburned Hydrocarbons (HC)
Particulates (PM)
Sulfur Dioxide (SO2)
Oxygen (O2)
Ozone (O3)
15,359 Ton/d
6,826 Ton/d
2,160 Ton/d
PROCESSING UNITS AND EQUIPMENT (3)
5,374 Ton/d
Potencia = 100 MW
Energía = 1,354 BFOE/d
2,646 Ton CO2/d
COGENERATION UNIT OF TALARA REFINERY

## Slide 4
PRODUCT | VOLUME | UNIT OF MEASURE | HEATING VALUE | UNIT OF MEASURE | PRODUCCIÓN DE CO2 (kg/1,000 ft3) | ENERGY PRODUCED (MMBTU)
NATURAL GAS | 136,456 | CUBIC FEET | 954.963 | BTU/SCF | 59.32 | 130
FUEL GAS | 3’844,330 | CUBIC FEET | 793.634 | BTU/SCF | 48.24 | 3,051
FLEXIGAS | 145’423,703 | CUBIC FEET | 130.376 | BTU/SCF | 14.13 | 18,960
LIGHT NAPHTHA | 0 | BARRELS | 4’440,264 | BTU/BBL | 66,287 | 0
TOTAL | 149’404,489 | CUBIC FEET | - | - | - | 22,141
CARGAS DE ALIMENTACIÓN DE LA UNIDAD DE COGENERACIÓN ELÉCTRICA
OPERACIÓN NORMAL (BASE DIARIA)

## Slide 5
PRODUCT | PORCENTAJE
Nitrógeno | 0.08
Dióxido de Carbono | 0.49
Metano | 93.08
Etano | 5.95
Propano | 0.01
N-Butano | 0.02
N-Pentano | 0.33
Oxígeno | 0.04
TOTAL | 100.00
COMPOSICIÓN DEL GAS NATURAL
EL CO2 TOTAL PRODUCIDO ES EL CO2 ORIGINAL MÁS EL CO2
PRODUCTO DE LA COMBUSTIÓN.
8,132 kg de Dióxido de Carbono por día

## Slide 6
PRODUCT | PORCENTAJE
Hidrógeno | 26.81
Nitrógeno | 2.75
Agua | 0.68
Monóxido de Carbono | 2.62
Dióxido de Carbono | 7.00
Metano | 42.05
Eteno | 3.43
Etano | 11.40
Propeno | 0.46
Propano | 0.63
Iso-Buteno | 0.78
Otros | 1.39
TOTAL | 100.00
COMPOSICIÓN DEL GAS COMBUSTIBLE
200,412 kg de Dióxido de Carbono
EL CO2 TOTAL PRODUCIDO ES EL CO2 ORIGINAL MÁS EL CO2
PRODUCTO DE LA COMBUSTIÓN.

## Slide 7
PRODUCT | PORCENTAJE
Hidrógeno | 15.39
Nitrógeno | 49.18
Agua | 5.28
Monóxido de Carbono | 25.14
Dióxido de Carbono | 4.17
Metano | 0.83
TOTAL | 100.00
COMPOSICIÓN DEL FLEXIGAS
2’437,904 kg de Dióxido de Carbono
EL CO2 TOTAL PRODUCIDO ES EL CO2 ORIGINAL MÁS EL CO2
PRODUCTO DE LA COMBUSTIÓN.